EP 208 PROBLEM HOUR QUESTION FOR FINAL EXAM

PROBLEM 1

An integer variable x of 4 bytes (32 bit) is stored in the computer memory

as follows:

00000000 00000000 00000000 01100101

Evaluate the value of x in base-10 and in base-16?

PROBLEM 2

a) Using Taylor's expansion derive the following Newton-Raphson iterative

formula for finding the root of a function f(x):

x[i+1] = x[i] - f(x[i]) / f'(x[i])

b) Using the Newton-Raphson method evaluate the root of the

function f(x) = ex - 3x2, which is near 1.0, to an accuracy

of at least 2 decimal places. Show the result of each iteration.

PROBLEM 3

| A spring-mass system is governed by the 2nd order D.E. where the mass is m = 1.01 kg, the spring constant is k = 10 N/m, v = dx/dt is the velocity in m/s and x is the displacement in m. Using a time step of h = dt = 0.1 s, evolve the system for 1 second. Write a computer program to solve the position x and velocity v of the mass via Euler Method. |  |
| --- | --- |

PROBLEM 4

A nucleus of an atom has a probability of decaying that is described by the pdf

f(t) = 0.1 exp(-0.1t) where t≥0 is the time in seconds.

Determine the probability that the nucleus survives 20 seconds.

PROBLEM 5

Table shows experimental results of a freely falling body.

t(s)| 0.000  0.200  0.400  0.600  0.800  1.000

----+-------------------------------------------

y(m)| 0.000  1.960  0.785  1.767  3.141  4.908

where t is the time measured in seconds and y is the distance measured in meter.

Using linear Least square method,

a) determine gravitational acceleration, g

b) calculate the regression coefficient.

_______________________________________________________________________________________

May 2010