EP 208 PROBLEM HOUR (16 Mar 2016)

PROBLEM 1

| Upward velocity (v) in m/s of a rocket as a function of time (t) in seconds is given by: V = 18*sqrt(t)*exp(-t**2/200) Assume that the position of the rocket is y=0 at t=0. Using Simplson’s Method find find the distance travelled by the rocket for the first 10 seconds use n = 6 parts. |  |
| --- | --- |

Question 2 [20%]

| Design an optimum semi-cylindrical trough having walls of negligible thickness. The container is to hold V = 0.3 m3 waste water. The material used for making up the container has the cost of 125.0 TL/m2. Design the container so that the total cost is minimized if the radius and the height of the trough are r and h respectively. |  |
| --- | --- |

Write down the cost function and find the analytical result of the values of r and h that minimize the cost.

Question 3 [20%]

Given the function f(x) = e−x – x. Determine the root of f(x) to an accuracy of at least 5% .

Use Newton-Raphson method and fill the table. (Take initial guess x0 = 2.0)

Question 4 [20%]

Using CDA and CDA2  with h = 0.1, compute the first derivative and second derivative of the function

at x = 2.5.

# Text boxes

r

h

open

| iter | x | Error Estimate |
| --- | --- | --- |
| 0 | 2.0000 | 0.0000 |
| 1 |  |  |
| 2 |  |  |
| 3 |  |  |
| ROOT = |  |